## Slide 1: IntruSense: An Enhanced Physical Security System using UWB
Shrenik Changede, Ashutosh Dhekne
HotMobile 2022

## Slide 2: Physical Security is a Multi-Billion Dollar Industry
https://www.prnewswire.com/news-releases/physical-security-market-worth-140-0-billion-by-2026--exclusive-research-by-marketsandmarkets-301467445.html
We forecast the market will reach $56.76Bn in 2024.
https://www.researchandmarkets.com/reports/4858655/the-physical-security-business-2019-to-2024
https://www.researchandmarkets.com/reports/5302516/home-security-systems-global-market-trajectory

## Slide 3: Physical Security is a Multi-Billion Dollar Industry
https://www.prnewswire.com/news-releases/physical-security-market-worth-140-0-billion-by-2026--exclusive-research-by-marketsandmarkets-301467445.html
We forecast the market will reach $56.76Bn in 2024.
https://www.researchandmarkets.com/reports/4858655/the-physical-security-business-2019-to-2024
https://www.researchandmarkets.com/reports/5302516/home-security-systems-global-market-trajectory

## Slide 4: Tools at our Disposal
Magnetic Ingress-Egress Sensors
IR Motion Sensors
Cameras

## Slide 5: Tools at our Disposal
Magnetic Ingress-Egress Sensors
IR Motion Sensors
Cameras
Room-level coverage
Multiple expensive devices
Triggered by friendlies
Large data processing
Large bandwidth needs
Issues

## Slide 6: Our Goal
https://housing.gatech.edu/building/tenth-and-home-bldg-f
Beyond a room – cover a large indoor space
Inexpensive, easy to deploy
Low data and bandwidth overhead
Allow presence of friendly entities
http://www.tyler-morgan.com/#/smile-train/

## Slide 7
Through a wireless sensing approach to physical security

## Slide 8
IntruSense:
An Enhanced Physical Security System using UWB

## Slide 9: Core Intuition

## Slide 10: Core Intuition

## Slide 11: Core Intuition
A static reflection pattern is observed
The reflections describe the wireless channel’s impulse response

## Slide 12: Core Intuition
An occupied space shows a different reflection pattern

## Slide 13: Core Intuition
Movement causes this pattern to change over time
https://www.pinterest.com.au/pin/361836151311622239/

## Slide 14
We use the changes in channel impulse response (CIR) to detect intrusion

## Slide 15: Sounds Simple, But…
Wireless signals travel at speed of light
  Distinguishing reflections requires nanosecond level precision (a billionth of a second)
Need a technology that covers a rather large indoor space
  mmWave vs WiFi vs UWB tradeoffs
How to ignore disturbances of known entities?
  Need a localization-based solution

## Slide 16: Sounds Simple, But…
Wireless signals travel at speed of light
  Distinguishing reflections requires nanosecond level precision (a billionth of a second)
Need a technology that covers a rather large indoor space
  mmWave vs WiFi vs UWB tradeoffs
How to ignore disturbances of known entities?
  Need a localization-based solution
Wide-bandwidth provides nanosecond CIR
Allows robust localization
Large coverage

## Slide 17: What is Ultra-wideband (UWB)?
Ultra wide-band is the technology ratified by 802.15.4a and 802.15.4z standards
500MHz or 1GHz bands in the 3.1–10.6 GHz range
Very low power -41.3dBm/Hz
Very low data rates 110kbps/850kbps/6.8Mbps
Long Range Indoors 50-70 meters
  Receiver sensitivity at -106dB/500MHz (1% err)
https://www.decawave.com/wp-content/uploads/2020/04/DW1000_Datasheet.pdf
https://www.qorvo.com/design-hub/ebooks/ultra-wideband-for-dummies
UWB
3.1-10.6GHz

## Slide 18: What is Ultra-wideband (UWB)?
Ultra wide-band is the technology ratified by 802.15.4a and 802.15.4z standards
500MHz or 1GHz bands in the 3.1–10.6 GHz range
Very low power -41.3dBm/Hz
Very low data rates 110kbps/850kbps/6.8Mbps
Long Range Indoors 50-70 meters
  Receiver sensitivity at -106dB/500MHz (1% err)
https://www.decawave.com/wp-content/uploads/2020/04/DW1000_Datasheet.pdf
https://www.qorvo.com/design-hub/ebooks/ultra-wideband-for-dummies
UWB
3.1-10.6GHz

## Slide 19: What is Ultra-wideband (UWB)?
https://www.decawave.com/wp-content/uploads/2020/04/DW1000_Datasheet.pdf
https://www.qorvo.com/design-hub/ebooks/ultra-wideband-for-dummies
UWB
3.1-10.6GHz
Ultra wide-band is the technology ratified by 802.15.4a and 802.15.4z standards
500MHz or 1GHz bands in the 3.1–10.6 GHz range
Very low power -41.3dBm/Hz
Very low data rates 110kbps/850kbps/6.8Mbps
Long Range Indoors 50-70 meters
  Receiver sensitivity at -106dB/500MHz (1% err)
not
^
X
X
X
X
X
https://www.cnet.com/tech/services-and-software/verizon-apple-u1-ultra-wideband-not-related/

## Slide 20: Where is UWB used?

## Slide 21: Innovations in IntruSense
We develop 4 models of security systems
Each uses progressively more complex wireless sensing logic.

## Slide 22: Sneak Preview
IntruSense Model 1
Detects line-of-sight obstruction
IntruSense Model 2
Detects disturbances to reflection patterns
IntruSense Model 3
Ignore movements of friendlies
IntruSense Model 4
Single central RADAR system
We develop 4 models of security systems
Each uses progressively more complex wireless sensing logic.

## Slide 23: Innovations in IntruSense
We develop 4 models of security systems
Each uses progressively more complex wireless sensing logic.
IntruSense Model 1
Detects line-of-sight obstruction

## Slide 24
UWB performs two-way ranging
Calculates distance between two devices
Across Doorway
Ingress/egress points
UWB 1
UWB 2
Line of sight
UWB 1
UWB 2
IntruSense Model 1
Detects line-of-sight obstruction

## Slide 25
IntruSense Model 1
Detects line-of-sight obstruction
Measured distance changes due to LOS blockage.
Across Doorway
Ingress/egress points
UWB 1
UWB 2
Line of sight

## Slide 26
IntruSense Model 1
Detects line-of-sight obstruction
Measured distance changes due to LOS blockage.
Across Doorway
Ingress/egress points
UWB 1
UWB 2
Line of sight

## Slide 27
IntruSense Model 2
Detects disturbances to reflection patterns

## Slide 28
Measure unoccupied indoor space’s CIR using multiple UWB
UWB 1
UWB 2
UWB 3
IntruSense Model 2
Detects disturbances to reflection patterns

## Slide 29
Measured disturbances to the observed CIR
UWB 1
UWB 2
UWB 3
Intruder disturbs NLOS
Reflection
IntruSense Model 2
Detects disturbances to reflection patterns

## Slide 30
IntruSense Model 3
Ignore movements of friendlies

## Slide 31
IntruSense Model 3
Ignore movements of friendlies
Can we arm the security system even when the space is occupied?

## Slide 32
IntruSense Model 3
Ignore movements of friendlies
Can we arm the security system even when the space is occupied?
Pets
Elderly
Guards

## Slide 33
IntruSense Model 3
Ignore movements of friendlies
Can we arm the security system even when the space is occupied?
Pets
Elderly
Guards
Not possible using IR motion detectors, cameras, etc.
False alarms are frequent

## Slide 34
IntruSense Model 3
Ignore movements of friendlies
Pets
Friendlies wear a UWB device
IntruSense localizes this friendly device
Ignores CIR changes in those locations
UWB
Collar
Detected Pet Location

## Slide 35
IntruSense Model 3
Ignore movements of friendlies
Friendly UWB device performs active localization with the security system
Security system ignores CIR changes in the vicinity of expected location
Raises alarm when unmatched reflections occur
UWB 1
UWB 2
UWB 3
Unmatched Reflection
Reflection matches known location
Active Localization

## Slide 36
IntruSense Model 4
Single central RADAR system

## Slide 37
IntruSense Model 4
Single central RADAR system
Model 3 requires multiple UWB devices.
Can we create a single central system, instead?
1
2
Active Localization
Ignored
Reflection raises alarm
3

## Slide 38
IntruSense Model 4
Single central RADAR system
Model 3 requires multiple UWB devices.
Can we create a single central system, instead?
1
2
Active Localization
Ignored
Reflection raises alarm
3
1
3
2
Receivers saturate, need to ignore direct signal.
Future Work

## Slide 39: Implementation
Decawave DWM1000 UWB
Buzzer
\
Object to be protected
At home preliminary tests
Attempting to steal an object demo

## Slide 40: Short Demo Video of IntruSense

## Slide 41: A Potential Solution to the UWB Radar problem
Time in nanoseconds (within a packet) 
High Amplitude
Low Amplitude
Strong direct-path signal
Weaker direct-path signal
Other reflections appear weak
Other reflections appear stronger
2-antenna system
1-antenna system
/2
Work in Progress

## Slide 42: Summary
IntruSense Model 1
Detects line-of-sight obstruction
IntruSense Model 2
Detects disturbances to reflection patterns
IntruSense Model 3
Ignore movements of friendlies
IntruSense Model 4
Single central RADAR system

## Slide 43: Conclusion
We are just getting started.
Perimeter fencing, home security, safeguarding valuables at a museum, etc. could all benefit from IntruSense.
IntruSense ignores friendlies while still monitoring an indoor space
We see a promise in using wireless sensing approach for physical security problems