## Slide 3
Notes: Paris town hall

## Slide 5: Welcome back!
Optional project 0 is out.
Project 1 will be out soon.
Today
  Image projection - Szeliski 2.1 (2.1.4 in particular)
  Filtering – Szeliski 3.2

## Slide 6
Notes: From Frank Dellaert’s fall 2025 course policy

## Slide 7: The Geometry of Image Formation
Mapping between image and world coordinates
  Pinhole camera model
  Projective geometry
    Vanishing points and lines
  Projection matrix

## Slide 8: What do you need to make a camera from scratch?

## Slide 9: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide source: Seitz

## Slide 10: Pinhole camera
Idea 2: add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Slide source: Seitz
Notes: Q: How does this transform the image? A: It gets inverted

## Slide 11: Pinhole camera
Figure from Forsyth
f
f = focal length
c = center of the camera
c

## Slide 12: Camera obscura: the pre-camera
Known during classical period in China and Greece (e.g. Mo-Ti, China, 470BC to 390BC)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys

## Slide 13: Camera Obscura used for Tracing
Lens Based Camera Obscura, 1568

## Slide 14: Accidental Cameras
Accidental Pinhole and Pinspeck Cameras Revealing the scene outside the picture. Antonio Torralba, William T. Freeman

## Slide 15: Accidental Cameras

## Slide 16
Notes: Partial eclipse

## Slide 17
https://www.reddit.com/r/Utah/comments/177ymi6/the_partial_eclipse_shadow_through_my_trees_st/
Notes: Partial eclipse

## Slide 18: First Photograph
Oldest surviving photograph
  Took 8 hours on pewter plate
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 20
“Louis Daguerre—the inventor of daguerreotype—shot what is not only the world's oldest photograph of Paris, but also the first photo with humans. The 10-minute long exposure was taken in 1839 in Place de la République and it's just possible to make out two blurry figures in the left-hand corner.”
Source

## Slide 21
Great history lesson on the chemistry and engineering challenges of early photography from the “Technology Connections” YouTube channel.
https://www.youtube.com/watch?v=wbbH77rYaa8&list=PLv0jwu7G_DFV6yW240e6CbiwCLaZ0Z6PV

## Slide 22
Slide credit Fei Fei Li

## Slide 23: Projective Geometry
What is lost?
Length
Which is closer?
Who is taller?

## Slide 24: Length and area are not preserved
Figure by David Forsyth
B’
C’
A’

## Slide 25: Projective Geometry
What is lost?
Length
Angles
Perpendicular?
Parallel?

## Slide 26: Projective Geometry
What is preserved?
Straight lines are still straight

## Slide 27
The pinhole camera model preserves straight lines, but real cameras might not
Notes: From https://alex4d.com/final_cut_plugins/alex4d-free-2/item/7-alex4d-wide-angle-fix-effect

## Slide 28: Vanishing points and lines
Parallel lines in the world intersect in the image at a “vanishing point”
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 29: Vanishing points and lines
o
Vanishing Point
o
Vanishing Point
Vanishing Line
Notes: Go to board, sketch out various properties of vanishing points/lines
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 30: Vanishing points and lines
Vanishing
point
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 31: Projection: world coordinatesimage coordinates
Camera Center (0, 0, 0)
.
.
.
f
z
y
.
v’
u’
If x = 2, y = 3, z = 5, and f = 2 What are u’ and v’?
3
5
2
?
Notes: Being a little loose about coordinates vs lengths
u and v prime because they are in the same coordinate system as x, y, and z but in later slides u and v will be –u’ and –v’ because they are in their own coordinate system which is mirrored

## Slide 32: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u
How do we handle the general case?

## Slide 33: Interlude: why does this matter?

## Slide 34: Relating multiple views

## Slide 38: DepthAnything V3 Reconstruction

## Slide 39: DepthAnything V3 Reconstruction

## Slide 41: VGGT Reconstruction

## Slide 44: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u
How do we handle the general case?

## Slide 45: Homogeneous coordinates
Conversion
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 46: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 47: Basic geometry in homogeneous coordinates
Line equation: ax + by + c = 0
Append 1 to pixel coordinate to get homogeneous coordinate
Line given by cross product of two points
Intersection of two lines given by cross product of the lines

## Slide 48: Another problem solved by homogeneous coordinates
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
Intersection of parallel lines
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 49
Slide Credit: Savarese
Projection matrix
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,t
X
x
Notes: We can use homogeneous coordinates to write camera matrix in linear form.

## Slide 50
Object Recognition (CVPR 2006)

## Slide 51
Inserting photographed objects into images (SIGGRAPH 2007)
Original
Created

## Slide 52: Pinhole Camera Model
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)

## Slide 53
K
Slide Credit: Savarese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
Notes: Work through equations for u and v on board

## Slide 54
Slide Credit: Savarese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
Notes: Work through equations for u and v on board

## Slide 55: Remove assumption: center pixel is (0,0)
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 56: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 57: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 58: Oriented and Translated Camera
Ow
iw
kw
jw
t
R
X
x

## Slide 59: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 60: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 61: Allow camera rotation

## Slide 62: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 63: Vanishing Point = Projection from Infinity

## Slide 64: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 65: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 66: Field of View (Zoom, focal length)

## Slide 67
Suppose we have two 3D cubes on the ground facing the viewer, one near, one far.
What would they look like in perspective?
What would they look like in weak perspective?
Photo credit: GazetteLive.co.uk

## Slide 68: Beyond Pinholes: Radial Distortion
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 69: Things to remember
3D -> 2D causes some weirdness in geometric relationships
Pinhole camera model and camera projection matrix
Homogeneous coordinates
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 70: Reminder: read your book
Lectures have assigned readings
Szeliski 2.1 and especially 2.1.4 cover the geometry of image formation

## Slide 71: New Topic: Image Filtering
Computer Vision
James Hays
Many slides by Derek Hoiem

## Slide 72
Project 1
BBC Clip: https://www.youtube.com/watch/OlumoQ05gS8

## Slide 74
Slide credit Fei Fei Li

## Slide 75
Slide credit Fei Fei Li

## Slide 76
Slide credit Fei Fei Li

## Slide 77: Hybrid Images
A. Oliva, A. Torralba, P.G. Schyns, “Hybrid Images,” SIGGRAPH 2006

## Slide 78: Upcoming classes: two views of filtering
Image filters in spatial domain
  Filter is a mathematical operation of a grid of numbers
  Smoothing, sharpening, measuring texture
Image filters in the frequency domain
  Filtering is a way to modify the frequencies of images
  Denoising, sampling, image compression

## Slide 79: Image filtering (or convolution)
Image filtering: compute a simple function of local neighborhood at each position
Really important!
  Manipulate images
    Denoise, resize, increase contrast, remove high frequencies, etc. (Project 1)
  Extract information from images
    Texture, edges, distinctive points, etc. (Project 2)
    Deep Convolutional Networks (Project 3 and 4)

## Slide 80
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Example: box filter

## Slide 81
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 82
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | ? |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 83
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 84
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 85
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 86
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 87
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 88
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 89
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 90
What does it do?
Returns the average of each neighborhood
Smooths an image (removes sharp features, removes some high spatial frequency features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 91
Smoothing with box filter

## Slide 92: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 93: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 94: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 95: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 96: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 97: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Source: D. Lowe

## Slide 98: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Source: D. Lowe
0
0
0
0
1
0
0
0
0
+
-1/9
-1/9
-1/9
-1/9
8/9
-1/9
-1/9
-1/9
-1/9

## Slide 99: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences w.r.t. local average
Source: D. Lowe
-1/9
-1/9
-1/9
-1/9
17/9
-1/9
-1/9
-1/9
-1/9
0
0
0
0
1
0
0
0
0
+
-1/9
-1/9
-1/9
-1/9
8/9
-1/9
-1/9
-1/9
-1/9

## Slide 100: Sharpening
Source: D. Lowe

## Slide 101: Other filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel

## Slide 102: Other filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel
Notes: Questions at this point?

## Slide 103: Filtering vs. Convolution
2d filtering
2d convolution
I=image, size m x n
f=filter, size k x l
In Python you can use https://docs.scipy.org/doc/scipy/reference/generated/scipy.signal.convolve2d.html
“Many readers will skim over formulas on their first reading of your exposition. Therefore, your sentences should flow smoothly when all but the simplest formulas are replaced by “blah” or some other grunting noise.” - Donald Knuth.

## Slide 104
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian
Notes: e^0 = 1, e^-1 = .37, e^-2 = .14, etc.

## Slide 105
Smoothing with Gaussian filter

## Slide 106
Smoothing with box filter

## Slide 107: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
  Images become more smooth
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width σ√2
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 108: Separability of the Gaussian filter
Source: D. Lowe

## Slide 109: Separability example
*
*
=
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:
Notes: Convolution vs filtering doesn’t matter here because the filter is symmetric

## Slide 110: Separability
Why is separability useful in practice?

## Slide 111: Some practical matters

## Slide 112: Practical matters
How big should the filter be?
Values at edges should be near zero
Rule of thumb for Gaussian: set filter half-width to about 3 σ

## Slide 113: Practical matters
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner

## Slide 114: Next class: Light and Color and Thinking in Frequency